## Slide 1
ESP32-S2 Implementation (single buffer / no panel back buffer)
GCLK + Colour Data (send continuously)
VSYNC
I2S Peripheral (24bit LCD Mode)
Continuous output using ESP32-S2 I2S Peripheral LCD Mode. Not able to interrupt.
VSYNC happens continuously. Pixel drawn to screen will show immediately.
Call to mbi_update() does nothing.
Not enough memory on ESP32-S2 for separate GCLK (PWM output) and colour data buffers.
ESP32-S3 Implementation (double buffer / panel back buffer)
GCLK
SPI2 Peripheral (8Bit / Octal SPI)
GCLK is continuously sent out if there’s no VSYNC.
Next frame’s pixel data is sent ‘in the background’ as required using the LCD interface.
Upon call of mbi_update(), GCLK (PWM output) is paused whilst VSYNC (sent via LCD interface) occurs.
GCLK is restarted with new display output shown immediately. This occurs in < 1 millisecond.
Colour Data
LCD Peripheral (16bit Mode)
VSYNC